## Slide 1: Quadratic vs. mixed elements
Mihai Francu, University of Copenhagen
Daniele Panozzo, New York University

## Slide 2: The problem
What is the best (low cost, low memory) method to use for incompressibility (with tetrahedral meshes)?
  Standard FEM with quadratic (P2) elements, OR
  Mixed FEM with P2/P1 or even P1/P1
Daniele: Why not use P2 all the time?
Mihai: Why not use P1/P1 for linear meshes?
Which mixed formulation for incompressible elasticity should we use?

## Slide 3: Questions
How hard is it to find an experiment where P2 locks?
How can we encourage locking?
  Get very close to 0.5 Poisson ratio
  Low quality meshes (bad elements)
  Nonlinear or anisotropic materials
  Non-homongeneous bodies (stiffness distribution)
  Boundary conditions and contact
How can we measure locking?
  Compare error to P4 high-res ground truth
  Non-smooth stress distribution

## Slide 4: Displacement field

## Slide 5: Stress field

## Slide 6: Standard FEM
P1 behaves very badly
P2 behaves very well (no apparent locking)
P3 should be better
P4 is locking free according to theory

## Slide 7: Mixed FEM
Always (almost) locking free
Care must be taken when choosing the pressure elements
P1/P0 will probably lock
P1/P1 (naïve) is not “stable”, but avoids locking in practice
P2/P1 is guaranteed to work
Thumb rule: Pn/Pn-1

## Slide 8: Solution
Compare mixed and standard FEM. : P1, P2, P3, P4, P1/P1, P2/P1
Optionally P1/P0, P2/P0
Metrics: Time, Accuracy (displacement, and stress), Memory
Validate results and ground truth

## Slide 9: Experiments
Quasi-static
Compressed box with Dirichlet boundary conditions (2D,3D)
Cantilever (2D,3D)
Tube with internal pressure (2D,3D)
Plate with hole (2D)
T-beam (2D)
Two layered material, i.e. different stiffness across elements (TBD)
Some kind of dynamic experiment

## Slide 10: Comparison methodology
We need to devise a way to compare FEM simulation results:
By deformed geometry (surface OBJ)
By displacement field (Paraview)
By stress field (Paraview)
Error from ground truth (TBD)
VTK files and Paraview seem to be the best way to compare all.

## Slide 11: Export format
Two options:
  Super-sample over a linear mesh (PolyFEM)
  Use the VTK file format and Paraview for any order
Both are tricky
First one is painful to replicate in every simulator
Second one assumes knowledge about of the basis functions
Paraview supports Lagrange and Bezier elements, but it’s a pain to export and vizualize the data (still possible though)
VTK with displacement and stress data at least is the winner

## Slide 12: PolyFEM vs. my simulator
P1 comparisons

## Slide 13: Geometry

## Slide 14: Displacement
Mine
PolyFEM

## Slide 15: Stress (elements)
Mine (magnitude)
PolyFEM (von Mises)

## Slide 16: Stress (nodes)
Mine (magnitude)
PolyFEM

## Slide 17: PolyFEM vs. my simulator
P2 comparisons

## Slide 18: Geometry
Mine
PolyFEM

## Slide 19: Displacement
Mine
PolyFEM

## Slide 20: Stress (nodes)
Mine (magnitude)
PolyFEM (von Mises)